## Slide 1: AP sigma environment setup SOP

## Slide 2: Outline
Introduction
Device preparation
Network route configuration
Environment setup steps

## Slide 3: Introduction
This SOP is designed for AP sigma testing, including following programs:
  WMMPS
  TGn
  PMF
  TGac
  WPA2 security improvement

## Slide 4: Device preparation
One notebook(CA notebook)
  With Windows OS and connect with UCC and the test device
One test device(APUT)
  Connecting to the notebook with USB cable

## Slide 5: Network route configuration
Control network
USB cable
Wireless network
Data network
Control network switch
(192.168.x.x)
Data network switch
(192.165.x.x)
eth1
rndis
rndis
ap0
bridge
bridge
192.165.100.99
APUT
CA
eth0
192.168.250.99
192.165.100.162
usb cable
UCC
Testbed APs
Testbed STAs

## Slide 6: Environment setup steps (1/4)
Prepare one yocto board as DUT (APUT) , and one notebook as control agent notebook (CA). Connect APUT to CA notebook with USB cable.
Fixed Wi-Fi mac address on APUT and also update the Mac address in init file
Use Ethernet cables to connect CA notebook to control network switch (192.168.x.x) & data network switch (192.165.x.x) separately
Confirm the DUT has rndis0 interface and use cmd to up the rndis0 intercace just like the following

## Slide 7: Environment setup steps (2/4)
5. Confirm the CA netbook will has 3 Ethernet interface (Eth0 ~Eth2)

## Slide 8: Environment setup steps (2/4)
Create a bridge between data network and USB network on CA notebook and set a available IP & net mask for this bridge network, eg. IP: 192.165.100.162, netmask: 255.255.0.0

## Slide 9: Environment setup steps (3/4)
Setup control network, eg. IP: 192.168.250.99, netmask: 255.255.255.0
  Set IP address of control network (192.168.x.x) on CA notebook for Eth0.
  Update init file
  Update PARA_SETUP.bat in AP sigma tool to modify CA_PORT to 9000
## PC Endpoint (WFA Traffic generator console)

## Slide 10: Environment setup steps (4/4)
Setup APUT’s wireless network, eg. IP: 192.165.100.99, netmask: 255.255.0.0
  Update init file
  Update PARA_SETUP.bat in AP sigma tool to modify PCENDPOINT’s ip address
## PC Endpoint (WFA Traffic generator console)

## Slide 11: Install & run sigma tool
Click the following script by sequence